C++ advanced notes

$ echo $? - checking if compiling was successful from command line	in Linux
$ echo %ERRORLEVEL% - checking if compiling was successful from	command line in Microsoft

output stream – we write to it, eg. cout, cerr, clog
input steam – we read from it, eg. cin

File redirection:
$ file.exe <infile >outfile - assuming $ is the system prompt and our addition program has been compiled into an executable file named file.exe, this command will read transactions from a file named infile and write its output to a file named outfile in the current directory.

plain char or bool:
- do not use in arithmetic expressions
- use them only to hold characters or truth values
- computations using char are especially problematic because char is signed on some machines and unsigned on others.

Problem of automating casting of int to unsigned int:
If we convert int to unsigned int and int is smaller than 0, than automatic conversion using modulus is executed. It is essential to remember that signed values are automatically converted to unsigned.

unsigned u = 10;
int i = -42;
std::cout << i + i << std::endl; // prints -84
std::cout << u + i << std::endl; // if 32-bit ints, prints	4294967264

different types of int literals:
- 20 - decimal
- 024 - octal
- 0x14 - hexadecimal

string literal:
The type of a string literal is array of constant chars. The compiler appends a null character (’\0’) to every string literal. Thus, the actual size of a string literal is one more than its apparent size. For example, the literal 'A' represents the single character A, whereas the string literal "A" represents an array of two characters, the letter A and the null character.

Escape sequences:
newline	\n	horizontal tab	\t	alert (bell)	\a
vertical tab	\v	backspace	\b double quote	\"
backslash	\\	question mark	\?	single quote \'
carriage return	\r	formfeed	\f

Example of escape sequences:
std::cout << "\tHi!\n";	// prints a tab followd by "Hi!" and a	newline

Specifying the Type of a literal:
L'a' // wide character literal, type is wchar_t
u8"hi!" // utf-8 string literal (utf-8 encodes a Unicode	character in 8 bits)
42ULL // unsigned integer literal, type is unsigned long long
1E-3F // single-precision floating-point literal, type is float
3.14159L // extended-precision floating-point literal, type is	long double

list initialization:
Using list initialization has one big advantage - the compiler will not let us list initialize variables of built-in type if the initializer might lead to the loss of information.

Example:
long double ld = 3.1415926536;
int a{ld}, b = {ld}; // error: narrowing conversion required
int c(ld), d = ld; // ok: but value will be truncated

Note!
Uninitialized objects of built-in type defined inside a function body have undefined value. Objects of class type that we do not explicitly initialize have a value that is defined by the class.

extern keyword:
To obtain a declaration that is not also a definition, we add the extern keyword and may not provide an explicit initializer:

Example:
extern int i; // declares but does not define i
int j; // declares and defines j

Any declaration that includes an explicit initializer is a definition. We can provide an initializer on a variable defined as extern, but doing so overrides the extern. An extern that has an initializer is a definition:

Example:
extern double pi = 3.1416; // definition

To use a variable in more than one file requires declarations that are separate from the variable’s definition. To use the same variable in multiple files, we must define that variable in one—and only one—file. Other files that use that variable must declare—but not define—that variable.

C++ keywords

references overview:
- When we define a reference, instead of copying the initializer’s value, we bind the reference to its initializer. Once initialized, a reference remains bound to its initial object.
- There is no way to rebind a reference to refer to a different object and therefore references must be initialized.
- A reference is not an object. Instead, a reference is just another name for an already existing object. Because references are not objects, we may not define a reference to a reference.

Example:
int a = 5;
int &b = a;

pointer overview:
- A pointer is a compound type that “points to” another type.
- Like references, pointers are used for indirect access to other objects.
- Unlike a reference, a pointer is an object in its own right.
- Pointers can be assigned and copied; a single pointer can point to several different objects over its lifetime.
- Unlike a reference, a pointer need not be initialized at the time it is defined.
- Like other built-in types, pointers defined at block scope have undefined value if they are not initialized.

The value (i.e., the address) stored in a pointer can be in one of four states:
1. It can point to an object.
2. It can point to the location just immediately past the end of an object.
3. It can be a null pointer, indicating that it is not bound to any object.
4. It can be invalid; values other than the preceding three are invalid.

Key Concept: Some Symbols Have Multiple Meanings
Some symbols, such as & and *, are used as both an operator in an
expression and as part of a declaration. The context in which a symbol is used determines what the symbol means:

Examples:
int i = 42;
int &r = i; // & follows a type and is part of a declaration;
r is a reference
int *p; // * follows a type and is part of a declaration;
p is a pointer
p = &i; // & is used in an expression as the address-of	operator
*p = i; // * is used in an expression as the dereference	operator
int &r2 = *p; // & is part of the declaration; * is the	dereference operator

In declarations, & and * are used to form compound types. In expressions, these same symbols are used to denote an operator. Because the same symbol is used with very different meanings, it can be helpful to ignore appearances and think of them as if they were different symbols.

null pointer - a null pointer does not point to any object.

Example:
int *p1 = nullptr; // equivalent to int *p1 = 0;

Examples of more complex references and pointers:
int ival = 1024;
int *pi = &ival; // pi points to an int
int **ppi = &pi; // ppi points to a pointer to an int
int *&r = p;	// r is a reference to the pointer p

Note!
To share a const object among multiple files, you must define the variable as extern.

Example:
extern const int bufSize = fcn();
constexpr:
- A constant expression is an expression whose value cannot change and that can be evaluated at compile time. A literal is a constant expression.
- Variables declared as constexpr are implicitly const and must be initialized by constant expressions.

Examples:
constexpr int mf = 20; // 20 is a constant expression
constexpr int limit = mf + 1; // mf + 1 is a constant expression
constexpr int sz = size(); // ok only if size is a constexpr	function

- Best Practices - generally, it is a good idea to use constexpr for variables that you intend to use as constant expressions.
- The types we can use in a constexpr are known as “literal types”.
- We cannot use a constexpr pointer to point to variables defined inside a function.
- It is important to understand that when we define a pointer in a constexpr declaration, the constexpr specifier applies to the pointer, not the type to which the pointer points.

Example:
const int *p = nullptr; // p is a pointer to a const int
constexpr int *q = nullptr; // q is a const pointer to int

type alias - is a name that is a synonym for another type. Type aliases let us simplify complicated type definitions, making those types easier to use.

Defining a type alias:
a) using typedef
typedef double wages; // wages is a synonym for double
typedef wages base, *p; // base is a synonym for double, p for	double*

Another example:
typedef int liczby_calkowite;
liczby_calkowite x = 10;
x += 10.6;
cout << x; // out: 20

b) using alias declaration (keyword ‘using’):
using liczby_calkowite = int; // liczby_calkowite is a synonym	for int

auto:
- auto tells the compiler to deduce the type from the initializer
auto item = v1 + v2; // item initialized to the result of v1 + v2

decltype - to define a variable with a type that the compiler deduces from an expression but do not want to use that expression to initialize the variable.

Example:
decltype(f()) sum = x; // sum has whatever type f returns

The way decltype handles top-level const and references differs subtly from the way auto does. When the expression to which we apply decltype is a variable, decltype returns the type of that variable, including top-level const and references.

Example:
const int ci = 0, &cj = ci;
decltype(ci) x = 0; // x has type const int
decltype(cj) y = x; // y has type const int& and is bound to x
decltype(cj) z; // error: z is a reference and must be	initialized

Warning!
Remember that decltype(( variable )) (note, double parentheses) is always a reference type, but decltype( variable ) is a reference type only if variable is a reference.

Example:
// decltype of a parenthesized variable is always a reference
decltype((i)) d; // error: d is int& and must be initialized
decltype(i) e; // ok: e is an (uninitialized) int

header guards – preprocessor directives to prevent multi including	of header files.

Example:
#ifndef SALES_DATA_H
#define SALES_DATA_H
#include <string>
struct Sales_data {
    std::string bookNo;
    unsigned units_sold = 0;
    double revenue = 0.0;
};
#endif

ways to initialize a string:

The string::size_type
Although we don’t know the precise type of string::size_type, we do know that it is an unsigned type big enough to hold the size of any string. Any variable used to store the result from the string size operation should be of type string::size_type. Because size returns an unsigned type, it is essential to remember that expressions that mix signed and unsigned data can have surprising results.

auto len = line.size(); // len has type string::size_type

To use size_type, we must name the type in which it is defined. A vector type always includes its element type.

vector<int>::size_type // ok
vector::size_type // error

Advice: Use the C++ Versions of C Library Headers
In addition to facilities defined specifically for C++, the C++ library incorporates the C library. Headers in C have names of the form name .h. The C++ versions of these headers are named c name—they remove the .h suffix and precede the name with the letter c. The c indicates that the header is part of the C library.

Example:
#include <math.h>	# C style
#include <cmath>	# C++ style

buffer overflow errors - attempting to subscript elements that do not exist. Such bugs are the most common cause of security problems in PC and other applications. A good way to ensure that subscripts are in range is to avoid subscripting altogether by using a range for whenever possible.

Example:
vector<int> v {0, 1, 2};
v[3] = 3	# error – buffer overflow

Note
If the container is empty, the iterators returned by begin and end are equal —they are both off-the-end iterators.

We may dereference only a valid iterator that denotes an element. Dereferencing an invalid iterator or an off-the-end iterator has undefined behavior.

Example:
string s("some string");
if (s.begin() != s.end()) { // make sure s is not empty
    auto it = s.begin(); // it denotes the first character in s
    *it = toupper(*it); // make that character uppercase
}

Key Concept: Generic Programming
Only a few library types, vector and string being among them, have the subscript operator. Similarly, all of the library containers have iterators that define the == and != operators. Most of those iterators do not have the < operator. By routinely using iterators and !=, we don’t have to worry about the precise type of container we’re processing.

A const_iterator behaves like a const pointer. Like a const pointer, a const_iterator may read but not write the element it denotes; an object of type iterator can both read and write. If a vector or string is const, we may use only its const_iterator type. With a nonconst vector or string, we can use either iterator or const_iterator.

Example:
vector<int>::iterator it; // it can read and write vector<int>	elements
string::iterator it2; // it2 can read and write characters in	a string
vector<int>::const_iterator it3; // it3 can read but not write	elements
string::const_iterator it4; // it4 can read but not write
characters

The begin and end iterators
The type returned by begin and end depends on whether the object on which they operator is const. If the object is const, then begin and end return a const_iterator; if the object is not const, they return iterator:

Example:
vector<int> v;
const vector<int> cv;
auto it1 = v.begin(); // it1 has type vector<int>::iterator
auto it2 = cv.begin(); // it2 has type vector<int>::const_iterator
auto it3 = v.cbegin(); // it3 has type vector<int>::const_iterator

Warning!
It is important to realize that loops that use iterators should not add elements to the container to which the iterators refer.

Character Arrays Are Special
Character arrays have an additional form of initialization: We can initialize such arrays from a string literal . When we use this form of initialization, it is important to remember that string literals end with a null character. That null character is copied into the array along with the characters in the literal:

Example:
char a1[] = {'C', '+', '+'}; // list initialization, no null
char a2[] = {'C', '+', '+', '\0'}; // list initialization,	explicit null
char a3[] = "C++"; // null terminator added
automatically
const char a4[6] = "Daniel"; // error: no space for the	null!
char arr[] = "adam";
for (const auto &c: arr){
if (c != '\0')	// null-terminated character
cout << c << endl;
}

The dimension of a1 is 3; the dimensions of a2 and a3 are both 4. The definition of a4 is in error. Although the literal contains only six explicit characters, the array size must be at least seven—six to hold the literal and one for the null.

No Copy or Assignment of c-style arrays
We cannot initialize an array as a copy of another array, nor is it legal to assign one array to another:

Example:
int a[] = {0, 1, 2}; // array of three ints
int a2[] = a; // error: cannot initialize one array with	another
a2 = a; // error: cannot assign one array to another
begin and end function
int ia[] = {0,1,2,3,4,5,6,7,8,9}; // ia is an array of ten ints
int *beg = begin(ia); // pointer to the first element in ia
int *last = end(ia); // pointer one past the last element in ia

// pbeg points to the first and pend points just past the last	element in arr
int *pbeg = begin(arr), *pend = end(arr);
// find the first negative element, stopping if we've seen all the	elements
while (pbeg != pend && *pbeg >= 0)
    ++pbeg;

Note
A pointer “one past” the end of a built-in array behaves the same way as the iterator returned by the end operation of a vector. In particular, we may not dereference or increment an off-the-end pointer.

As with iterators, subtracting two pointers gives us the distance between those pointers. The pointers must point to elements in the same array. The result of subtracting two pointers is a library type named ptrdiff_t.
auto n = end(arr) - begin(arr); // n is 5, the number of elements	in arr

Warning!
Unlike subscripts for vector and string, the index of the built-in subscript operator is not an unsigned type.

Conversion of c++ string to c-style string:
char *str = s; // error: can't initialize a char* from a string
const char *str = s.c_str(); // ok

The name c_str indicates that the function returns a C-style character string. That is, it returns a pointer to the beginning of a null-terminated character array that holds the same data as the characters in the string. The type of the pointer is const
char*, which prevents us from changing the contents of the array.

Note
To use a multidimensional array in a range for, the loop control variable for all but the innermost array must be references.

for (auto &row : ia)
    for (auto col : row)

The unary minus operator returns the result of negating a (possibly promoted) copy
of the value of its operand:

Example:
int i = 1024;
int k = -i; // i is -1024
bool b = true;
bool b2 = -b; // b2 is true!

For most operators, operands of type bool are promoted to int. In this case, the value of b is true, which promotes to the int value 1. That (promoted) value is negated, yielding -1. The value -1 is converted back to bool and used to initialize b2. This initializer is a nonzero value, which when converted to bool is true. Thus, the value of b2 is true!

The sizeof operator
The sizeof operator returns the size, in bytes, of an expression or a type name.

sizeof (type)
sizeof expr

Example:
Sales_data data, *p;
sizeof(Sales_data); // size required to hold an object of type	Sales_data
sizeof data; // size of data's type, i.e., sizeof(Sales_data)
sizeof p; // size of a pointer
sizeof *p; // size of the type to which p points, i.e.,	sizeof(Sales_data)
sizeof data.revenue; // size of the type of Sales_data's revenue	member
sizeof Sales_data::revenue; // alternative way to get the size of	revenue

The result of applying sizeof depends in part on the type involved:
• sizeof char or an expression of type char is guaranteed to be 1.
• sizeof a reference type returns the size of an object of the referenced type.
• sizeof a pointer returns the size needed hold a pointer.
• sizeof a dereferenced pointer returns the size of an object of the type to which the pointer points; the pointer need not be valid.
• sizeof an array is the size of the entire array. It is equivalent to taking the sizeof the element type times the number of elements in the array. Note that sizeof does not convert the array to a pointer.
• sizeof a string or a vector returns only the size of the fixed part of these types; it does not return the size used by the object’s elements.

Example:
// sizeof(ia)/sizeof(*ia) returns the number of elements in ia
constexpr size_t sz = sizeof(ia)/sizeof(*ia);
int arr2[sz]; // ok sizeof returns a constant expression

Operations precedence

The comma operator takes two operands, which it evaluates from left to right. Like the logical AND and logical OR and the conditional operator, the comma operator guarantees the order in which its operands are evaluated.

Arithmetic conversions examples:
bool flag; char cval;
short sval; unsigned short usval;
int ival; unsigned int uival;
long lval; unsigned long ulval;
float fval; double dval;
3.14159L + 'a'; // 'a' promoted to int, then that int converted	to long double
dval + ival; // ival converted to double
dval + fval; // fval converted to double
ival = dval; // dval converted (by truncation) to int
flag = dval; // if dval is 0, then flag is false, otherwise	true
cval + fval; // cval promoted to int, then that int converted	to float
sval + cval; // sval and cval promoted to int
cval + lval; // cval converted to long
ival + ulval; // ival converted to unsigned long
usval + ival; // promotion depends on the size of unsigned	short and int
uival + lval; // conversion depends on the size of unsigned int	and long

Explicit conversion

cast-name<type>(expression);

where type is the target type of the conversion, and expression is the value to be cast. If type is a reference, then the result is an lvalue. The cast-name may be one of static_cast, dynamic_cast, const_cast, and reinterpret_cast.

A static_cast is often useful when a larger arithmetic type is assigned to a smaller type.

Example:
// cast used to force floating-point division
double slope = static_cast<double>(j) / i;

A static_cast is also useful to perform a conversion that the compiler will not generate automatically. For example, we can use a static_cast to retrieve a pointer value that was stored in a void* pointer.

Example:
void* p = &d; // ok: address of any nonconst object can be	stored in a void*
// ok: converts void* back to the original pointer type
double *dp = static_cast<double*>(p);

A const_cast changes only a low-level const in its operand:

Example:
const char *pc;
char *p = const_cast<char*>(pc); // ok: but writing through p is
undefined

Conventionally we say that a cast that converts a const object to a nonconst type “casts away the const.” Once we have cast away the const of an object, the compiler will no longer prevent us from writing to that object. If the object was originally not a const, using a cast to obtain write access is legal. However, using a
const_cast in order to write to a const object is undefined.

A reinterpret_cast generally performs a low-level reinterpretation of the bit pattern of its operands.

Example:
int *ip;
char *pc = reinterpret_cast<char*>(ip);

Warning!
A reinterpret_cast is inherently machine dependent. Safely using
reinterpret_cast requires completely understanding the types involved as well as the details of how the compiler implements the cast.

Operation precedence

Null Statement
A null statement is useful where the language requires a statement but the program’s logic does not.

Example:
// read until we hit end-of-file or find an input equal to sought
while (cin >> s && s != sought)
    ; // null statement

Best Practices!
Null statements should be commented. That way anyone reading the code can see that the statement was omitted intentionally.

Note!
A block {…} is not terminated by a semicolon.

We also can define an empty block by writing a pair of curlies with no statements. An empty block is equivalent to a null statement.

Example:
while (cin >> s && s != sought)
    { } // empty block

Exceptions

Example:
// first check that the data are for the same item
if (item1.isbn() != item2.isbn())
    throw runtime_error("Data must refer to same ISBN");
// if we're still here, the ISBNs are the same
cout << item1 + item2 << endl;

In this code, if the ISBN s differ, we throw an expression that is an object of type runtime_error. Throwing an exception terminates the current function and transfers control to a handler that will know how to handle this error. The type runtime_error is one of the standard library exception types and is defined in the stdexcept header.

The general form of a try block is:
try {
    program-statements
} catch (exception-declaration) {
    handler-statements
} catch (exception-declaration) {
    handler-statements
} // . . .

Example:
while (cin >> item1 >> item2) {
    try {
        // execute code that will add the two Sales_items
        // if the addition fails, the code throws a runtime_error	// exception
    } catch (runtime_error err) {
        // remind the user that the ISBNs must match and prompt	// for another pair
        cout << err.what()
        << "\nTry Again? Enter y or n" << endl;
        char c;
        cin >> c;
        if (!cin || c == 'n')
        break; // break out of the while loop
    }
}

The C++ library defines several classes that it uses to report problems encountered in the functions in the standard library:
• The exception header defines the most general kind of exception class named exception. It communicates only that an exception occurred but provides no additional information.
• The stdexcept header defines several general-purpose exception classes

• The new header defines the bad_alloc exception type.
• The type_info header defines the bad_cast exception type.

The exception types define only a single operation named what. That function takes no arguments and returns a const char* that points to a C-style character string. The purpose of this C-style character string is to provide some sort of textual description of the exception thrown.

Function Return Type

The return type may not be an array type or a function type. However, a function may return a pointer to an array or a function.

Pointer or Reference Parameters and const

Because parameters are initialized in the same way that variables are initialized, it can be helpful to remember the general initialization rules. We can initialize an object with a low-level const from a nonconst object but not vice versa, and a plain reference must be initialized from an object of the same type.

Example:
int i = 42;
const int *cp = &i; // ok: but cp can't change i
const int &r = i; // ok: but r can't change i
const int &r2 = 42; // ok
int *p = cp; // error: types of p and cp don't match
int &r3 = r; // error: types of r3 and r don't match
int &r4 = 42; // error: can't initialize a plain reference from a	literal

// function that takes a reference to an int and sets the given object to zero
void reset(int &i) // i is just another name for the object	passed to reset
{
    i = 0; // changes the value of the object to which i refers
}
int i = 0;
const int ci = i;
string::size_type ctr = 0;
reset(&i); // error: calls the version of reset that has an int*	parameter
reset(&ci); // error: can't initialize an int* from a pointer to	a const int object
reset(i); // calls the version of reset that has an int&	parameter
reset(ci); // error: can't bind a plain reference to the const	object ci
reset(42); // error: can't bind a plain reference to a literal
reset(ctr); // error: types don't match; ctr has an unsigned type

Using const reference as parameter in a function call enables to use literals as parameters without a compilation error.

Example:
void find_char(const string &word, const char &c){};
find_char("Hello World", 'o');	// ok

Array Parameters

We cannot copy an array, and when we use an array it is (usually) converted to a pointer. Because we cannot copy an array, we cannot pass an array by value. Because arrays are converted to pointers, when we pass an array to a function, we are actually passing a pointer to the array’s first element.

Example:
// despite appearances, these three declarations of print are equivalent
void print(const int*);
void print(const int[]); // shows the intent that the function	takes an array
void print(const int[10]); // dimension for documentation purposes	(at best)

Regardless of appearances, these declarations are equivalent: Each declares a function with a single parameter of type const int*. When the compiler checks a call to print, it checks only that the argument has type const int*:

Example:
int i = 0, j[2] = {0, 1};
print(&i); // ok: &i is int*
print(j); // ok: j is converted to an int* that points to j[0]

Three common techniques used to manage pointer parameters:

a) Using a Marker to Specify the Extent of an Array

The first approach requires the array itself to contain an end marker. C-style character strings are an example of this approach. C-style strings are stored in character arrays in which the last character of the string is followed by a null character. Functions that deal with C-style strings stop processing the array when they see a null character:

Example:
void print(const char *cp)
{
    if (cp) // if cp is not a null pointer
        while (*cp) // so long as the character it points to is	not a null character
        cout << *cp++; // print the character and advance the	pointer
}

b) Using the Standard Library Conventions

A second technique is to pass pointers to the first and one past the last element in the array. This approach is inspired by techniques used in the standard library.

Example:
void print(const int *beg, const int *end)
{
// print every element starting at beg up to but not including end
    while (beg != end)
        cout << *beg++ << endl; // print the current element
        // and advance the pointer
}

int j[2] = {0, 1};
// j is converted to a pointer to the first element in j
// the second argument is a pointer to one past the end of j
print(begin(j), end(j)); // begin and end functions

c) Explicitly Passing a Size Parameter

A third approach is common in C programs and older C++ programs, is to define a second parameter that indicates the size of the array.

Example:
// const int ia[] is equivalent to const int* ia
// size is passed explicitly and used to control access to	elements of ia
void print(const int ia[], size_t size)
{
    for (size_t i = 0; i != size; ++i) {
        cout << ia[i] << endl;
    }
}

int j[] = { 0, 1 }; // int array of size 2
print(j, end(j) – begin(j));

Note
Again, the parentheses around *matrix are necessary:
int *matrix[10]; // array of ten pointers
int (*matrix)[10]; // pointer to an array of ten ints

main: Handling Command-Line Options

Command-line options are passed to main in two (optional) parameters:

int main(int argc, char *argv[]) { ... }
OR
int main(int argc, char **argv) { ... }

The first parameter, argc, passes the number of strings in that array. The second parameter, argv, is an array of pointers to C-style character strings.

When arguments are passed to main, the first element in argv points either to the name of the program or to the empty string. Subsequent elements pass the arguments provided on the command line. The element just past the last pointer is guaranteed to be 0.

Example:
prog -d -o ofile data0

argv[0] = "prog"; // or argv[0] might point to an empty string
argv[1] = "-d";
argv[2] = "-o";
argv[3] = "ofile";
argv[4] = "data0";
argv[5] = 0;

Warning!
When you use the arguments in argv, remember that the optional
arguments begin in argv[1]; argv[0] contains the program’s name, not user input.

Functions with Varying Parameters:

a) initializer_list Parameters

We can write a function that takes an unknown number of arguments of a single type by using an initializer_list parameter. An initializer_list is a library type that represents an array of values of the specified type. This type is defined in the initializer_list header.

Unlike vector, the elements in an initializer_list are always const values; there is no way to change the value of an element in an initializer_list.

Example:
initializer_list<string> ls; // initializer_list of strings

void error_msg(initializer_list<string> il)
{
    for (auto beg = il.begin(); beg != il.end(); ++beg)
        cout << *beg << " " ;
    cout << endl;
}

When we pass a sequence of values to an initializer_list parameter, we must enclose the sequence in curly braces:

Example:
// expected, actual are strings
if (expected != actual)
    error_msg({"functionX", expected, actual});
else
    error_msg({"functionX", "okay"})

b) Ellipsis Parameters

Ellipsis parameters are in C++ to allow programs to interface to C code that uses a C library facility named varargs. Generally an ellipsis parameter should not be used for other purposes.

Warning!
Ellipsis parameters should be used only for types that are common to both C and C++. In particular, objects of most class types are not copied properly when passed to an ellipsis parameter.

An ellipsis parameter may appear only as the last element in a parameter list and may take either of two forms:
void foo(parm_list, ...);
void foo(...);

Functions with No Return Value

Typically, void functions use a return to exit the function at an intermediate point.

Example:
void swap(int &v1, int &v2)
{
    // if the values are already the same, no need to swap, just	return
    if (v1 == v2)
        return;
    // if we're here, there's work to do
    int tmp = v2;
    v2 = v1;
    v1 = tmp;
    // no explicit return necessary
}

Functions with Return Value

Tip
One good way to ensure that the return is safe is to ask: To what preexisting object is the reference referring?

Call operator precedence

The call operator has the same precedence as the dot and arrow operators.

Example:
// call the size member of the string returned by shorterString
auto sz = shorterString(s1, s2).size();

char &get_val(string &str, string::size_type ix)
{
    return str[ix]; // get_val assumes the given index is valid
}
int main()
{
    string s("a value");
    cout << s << endl; // prints a value
    get_val(s, 0) = 'A'; // changes s[0] to A
    cout << s << endl; // prints A value
    return 0;
}

It may be surprising to see a function call on the left-hand side of an assignment. However, nothing special is involved. The return value is a reference, so the call is anlvalue. Like any other lvalue, it may appear as the left-hand operand of the assignment operator.

If the return type is a reference to const, then (as usual) we may not assign to the result of the call.

Example:
// return a reference to the shorter of two strings
const string &shorterString(const string &s1, const string
&s2)
{
    return s1.size() <= s2.size() ? s1 : s2;
}

shorterString("hi", "bye") = "X"; // error: return value is const

List Initializing the Return Value

Under the new standard, functions can return a braced list of values. As in any other return, the list is used to initialize the temporary that represents the function’s return.

Example:
vector<string> process()
{
    // . . .
    // expected and actual are strings
    if (expected.empty())
        return {}; // return an empty vector
    else if (expected == actual)
        return {"functionX", "okay"}; // return list-initialized	vector
    else
        return {"functionX", expected, actual};
}

Returning a Pointer to an Array

Because we cannot copy an array, a function cannot return an array. However, a function can return a pointer or a reference to an array. Unfortunately, the syntax used to define functions that return pointers or references to arrays can be intimidating. Fortunately, there are ways to simplify such declarations.
The most straightforward way is to use a type alias:

typedef int arrT[10]; // arrT is a synonym for the type array of	ten ints
using arrtT = int[10]; // equivalent declaration of arrT; see §	2.5.1 (p. 68)
arrT* func(int i); // func returns a pointer to an array of	five ints

Here arrT is a synonym for an array of ten ints. Because we cannot return an array, we define the return type as a pointer to this type.

Declaring a Function That Returns a Pointer to an Array

Type (*function(parameter_list))[dimension]

Example:
int (*func(int i))[10];

To understand this declaration, it can be helpful to think about it as follows:
• func(int) says that we can call func with an int argument.
• (*func(int)) says we can dereference the result of that call.
• (*func(int))[10] says that dereferencing the result of a call to func yields an array of size ten.
• int (*func(int))[10] says the element type in that array is int.

Using decltype

int odd[] = {1,3,5,7,9};
int even[] = {0,2,4,6,8};
// returns a pointer to an array of five int elements
decltype(odd) *arrPtr(int I)
{
    return (i % 2) ? &odd : &even; // returns a pointer to the	array
}

The return type for arrPtr uses decltype to say that the function returns a pointer to whatever type odd has. That object is an array, so arrPtr returns a pointer to an array of five ints. The only tricky part is that we must remember that decltype does not automatically convert an array to its corresponding pointer type. The type returned by decltype is an array type, to which we must add a * to indicate that arrPtr returns a pointer.

inline Functions Avoid Function Call Overhead

A function specified as inline (usually) is expanded “in line” at each call.

Example:
// inline version: find the shorter of two strings
inline const string &shorterString(const string &s1, const string &s2)
{
        return s1.size() <= s2.size() ? s1 : s2;
}

In general, the inline mechanism is meant to optimize small, straight-line functions that are called frequently. Many compilers will not inline a recursive function.

constexpr Functions

A constexpr function is a function that can be used in a constant expression. A constexpr function is defined like any other function but must meet certain restrictions: The return type and the type of each parameter in a must be a literal type, and the function body must contain exactly one return statement:

Example:
constexpr int new_sz() { return 42; }
constexpr int foo = new_sz(); // ok: foo is a constant expression

// scale(arg) is a constant expression if arg is a constant	expression
constexpr size_t scale(size_t cnt) { return new_sz() * cnt; }

int arr[scale(2)]; // ok: scale(2) is a constant expression
int i = 2; // i is not a constant expression
int a2[scale(i)]; // error: scale(i) is not a constant expression

Note
A constexpr function is not required to return a constant expression.

Debugging aid

The C++ compiler defines names that can be useful in debugging:
__func__ string literal containing the name of the function
__FILE__ string literal containing the name of the file
__LINE__ integer literal containing the current line number
__TIME__ string literal containing the time the file was compiled
__DATE__ string literal containing the date the file was compiled

Pointers to Functions

A function pointer is just that—a pointer that denotes a function rather than an object. Like any other pointer, a function pointer points to a particular type. A function’s type is determined by its return type and the types of its parameters. The function’s name is not part of its type.

Example:
// compares lengths of two strings
bool lengthCompare(const string &, const string &);

// pf points to a function returning bool that takes two const	string references
bool (*pf)(const string &, const string &); // uninitialized

Note
The parentheses around *pf are necessary. If we omit the parentheses, then we declare pf as a function that returns a pointer to bool:

// declares a function named pf that returns a bool*
bool *pf(const string &, const string &);

Using Function Pointers

When we use the name of a function as a value, the function is automatically converted to a pointer.

Example:
pf = lengthCompare; // pf now points to the function named	lengthCompare
pf = &lengthCompare; // equivalent assignment: address-of operator	is optional

We can use a pointer to a function to call the function to which the pointer points.

Example:
bool b1 = pf("hello", "goodbye"); // calls lengthCompare
bool b2 = (*pf)("hello", "goodbye"); // equivalent call
bool b3 = lengthCompare("hello", "goodbye"); // equivalent call

Function Pointer Parameters

Just as with arrays, we cannot define parameters of function type but can have a parameter that is a pointer to function. As with arrays, we can write a parameter that looks like a function type, but it will be treated as a pointer:

Example:
// third parameter is a function type and is automatically treated	as a pointer to function
void useBigger(const string &s1, const string &s2,
        bool pf(const string &, const string &));
// equivalent declaration: explicitly define the parameter as a	pointer to function
void useBigger(const string &s1, const string &s2,
        bool (*pf)(const string &, const string &));

Returning a Pointer to Function

The easiest way to declare a function that returns a pointer to function is by using a type alias:

Example:
using F = int(int*, int); // F is a function type, not a	pointer
using PF = int(*)(int*, int); // PF is a pointer type

Here we used type alias declarations to define F as a function type and PF as a pointer to function type. The thing to keep in mind is that, unlike what happens to parameters that have function type, the return type is not automatically converted to a pointer type. We must explicitly specify that the return type is a pointer type:

Example:
PF f1(int); // ok: PF is a pointer to function; f1 returns a	pointer to function
F f1(int); // error: F is a function type; f1 can't return a	function
F *f1(int); // ok: explicitly specify that the return type is a	pointer to function

CLASSES

Note
Functions defined in the class are implicitly inline.

Member functions access the object on which they were called through an extra, implicit parameter named this. When we call a member function, this is initialized with the address of the object on which the function was invoked. Because this is intended to always refer to “this” object, this is a const pointer.

Example:
std::string isbn() const { return this->bookNo; }

A const following the parameter list indicates that this is a pointer to const. Member functions that use const in this way are const member functions. The fact that this is a pointer to const means that const member functions cannot change the object on which they are called.

Example:
std::string isbn() const { return this->bookNo; }

Note
Objects that are const, and references or pointers to const objects, may call only const member functions.

Defining a Member Function outside the Class

Important to add class scope to function definition outside the class body.

Example:
double Sales_data::avg_price() const {
    if (units_sold)
        return revenue/units_sold;
    else
        return 0;
}

Defining a Function to Return “This” Object

Ordinarily, when we define a function that operates like a built-in operator, our function should mimic the behavior of that operator. The built-in assignment operators return their left-hand operand as an lvalue. To return an lvalue, our combine function must return a reference. Because the left-hand operand is a Sales_data object, the return type is Sales_data&.

Example:
Sales_data& Sales_data::combine(const Sales_data &rhs)
{
    units_sold += rhs.units_sold; // add the members of rhs into
    revenue += rhs.revenue; // the members of ''this''	object
    return *this; // return the object on which the function was	called
}

Defining extraction operator (print function)

Print function take a reference to its respective IO class type. The IO classes are types that cannot be copied, so we may only pass them by reference. Moreover, reading or writing to a stream changes that stream, so both functions take ordinary references, not references to const.

ostream &print(ostream &os, const Sales_data &item)
{
    os << item.isbn() << " " << item.units_sold << " "
       << item.revenue << " " << item.avg_price();
    return os;
}

Note
The compiler generates a default constructor automatically only if a class declares no constructors.

Constructor Initializer List

A constructor initializer list specifies initial values for one or more data members of the object being created. The constructor initializer is a list of member names, each of which is followed by that member’s initial value in parentheses (or inside curly braces). Multiple member initializations are separated by commas.

Example:
Sales_data(const std::string &s, unsigned n, double p):
        bookNo(s), units_sold(n), revenue(p*n) { }

Note
The only difference between using class and using struct to define a class is the default access level.

Tip
Ordinarily it is a good idea to group friend declarations together at the beginning or end of the class definition.

mutable Data Members

It sometimes (but not very often) happens that a class has a data member that we want to be able to modify, even inside a const member function. We indicate such members by including the mutable keyword in their declaration. A mutable data member is never const, even when it is a member of a const object. Accordingly, a const member function may change a mutable member.

Example:
class Screen {
public:
    void some_member() const;
private:
    mutable size_t access_ctr; // may change even in a const	object
    // other members as before
};
void Screen::some_member() const
{
    ++access_ctr; // keep a count of the calls to any member	function
    // whatever other work this member needs to do
}

Functions That Return *this

Function that return a reference to the object on which they are called. Functions that return a reference are lvalues, which means that they return the object itself, not a copy of the object.

Example:
// move the cursor to a given position, and set that character
myScreen.move(4,0).set('#');

these operations will execute on the same object. In this expression, we first move the cursor inside myScreen and then set a character in myScreen’s contents member. That is, this statement is equivalent to:

myScreen.move(4,0);
myScreen.set('#');

Had we defined move and set to return Screen, rather than Screen&, this statement would execute quite differently. In this case it would be equivalent to:

// if move returns Screen not Screen&
Screen temp = myScreen.move(4,0); // the return value would be	copied
temp.set('#'); // the contents inside myScreen would be unchanged

If move had a nonreference return type, then the return value of move would be a copy of *this. The call to set would change the temporary copy, not myScreen.

Note
A const member function that returns *this as a reference should have a return type that is a reference to const.

Tip
Definitions of type names usually should appear at the beginning of a class. That way any member that uses that type will be seen after the type name has already been defined.