C++ advanced notes

$ echo $? - checking if compiling was successful from command line	in Linux
$ echo %ERRORLEVEL% - checking if compiling was successful from	command line in Microsoft

output stream – we write to it, eg. cout, cerr, clog
input steam – we read from it, eg. cin

File redirection:
$ file.exe <infile >outfile - assuming $ is the system prompt and our addition program has been compiled into an executable file named file.exe, this command will read transactions from a file named infile and write its output to a file named outfile in the current directory.

plain char or bool:
- do not use in arithmetic expressions
- use them only to hold characters or truth values
- computations using char are especially problematic because char is signed on some machines and unsigned on others.

Problem of automating casting of int to unsigned int:
If we convert int to unsigned int and int is smaller than 0, than automatic conversion using modulus is executed. It is essential to remember that signed values are automatically converted to unsigned.

unsigned u = 10;
int i = -42;
std::cout << i + i << std::endl; // prints -84
std::cout << u + i << std::endl; // if 32-bit ints, prints	4294967264

different types of int literals:
- 20 - decimal
- 024 - octal
- 0x14 - hexadecimal

string literal:
The type of a string literal is array of constant chars. The compiler appends a null character (’\0’) to every string literal. Thus, the actual size of a string literal is one more than its apparent size. For example, the literal 'A' represents the single character A, whereas the string literal "A" represents an array of two characters, the letter A and the null character.

Escape sequences:
newline	\n	horizontal tab	\t	alert (bell)	\a
vertical tab	\v	backspace	\b double quote	\"
backslash	\\	question mark	\?	single quote \'
carriage return	\r	formfeed	\f

Example of escape sequences:
std::cout << "\tHi!\n";	// prints a tab followd by "Hi!" and a	newline

Specifying the Type of a literal:
L'a' // wide character literal, type is wchar_t
u8"hi!" // utf-8 string literal (utf-8 encodes a Unicode	character in 8 bits)
42ULL // unsigned integer literal, type is unsigned long long
1E-3F // single-precision floating-point literal, type is float
3.14159L // extended-precision floating-point literal, type is	long double

list initialization:
Using list initialization has one big advantage - the compiler will not let us list initialize variables of built-in type if the initializer might lead to the loss of information.

Example:
long double ld = 3.1415926536;
int a{ld}, b = {ld}; // error: narrowing conversion required
int c(ld), d = ld; // ok: but value will be truncated

Note!
Uninitialized objects of built-in type defined inside a function body have undefined value. Objects of class type that we do not explicitly initialize have a value that is defined by the class.

extern keyword:
To obtain a declaration that is not also a definition, we add the extern keyword and may not provide an explicit initializer:

Example:
extern int i; // declares but does not define i
int j; // declares and defines j

Any declaration that includes an explicit initializer is a definition. We can provide an initializer on a variable defined as extern, but doing so overrides the extern. An extern that has an initializer is a definition:

Example:
extern double pi = 3.1416; // definition

To use a variable in more than one file requires declarations that are separate from the variable’s definition. To use the same variable in multiple files, we must define that variable in one—and only one—file. Other files that use that variable must declare—but not define—that variable.

C++ keywords

references overview:
- When we define a reference, instead of copying the initializer’s value, we bind the reference to its initializer. Once initialized, a reference remains bound to its initial object.
- There is no way to rebind a reference to refer to a different object and therefore references must be initialized.
- A reference is not an object. Instead, a reference is just another name for an already existing object. Because references are not objects, we may not define a reference to a reference.

Example:
int a = 5;
int &b = a;

pointer overview:
- A pointer is a compound type that “points to” another type.
- Like references, pointers are used for indirect access to other objects.
- Unlike a reference, a pointer is an object in its own right.
- Pointers can be assigned and copied; a single pointer can point to several different objects over its lifetime.
- Unlike a reference, a pointer need not be initialized at the time it is defined.
- Like other built-in types, pointers defined at block scope have undefined value if they are not initialized.

The value (i.e., the address) stored in a pointer can be in one of four states:
1. It can point to an object.
2. It can point to the location just immediately past the end of an object.
3. It can be a null pointer, indicating that it is not bound to any object.
4. It can be invalid; values other than the preceding three are invalid.

Key Concept: Some Symbols Have Multiple Meanings
Some symbols, such as & and *, are used as both an operator in an
expression and as part of a declaration. The context in which a symbol is used determines what the symbol means:

Examples:
int i = 42;
int &r = i; // & follows a type and is part of a declaration;
r is a reference
int *p; // * follows a type and is part of a declaration;
p is a pointer
p = &i; // & is used in an expression as the address-of	operator
*p = i; // * is used in an expression as the dereference	operator
int &r2 = *p; // & is part of the declaration; * is the	dereference operator

In declarations, & and * are used to form compound types. In expressions, these same symbols are used to denote an operator. Because the same symbol is used with very different meanings, it can be helpful to ignore appearances and think of them as if they were different symbols.

null pointer - a null pointer does not point to any object.

Example:
int *p1 = nullptr; // equivalent to int *p1 = 0;

Examples of more complex references and pointers:
int ival = 1024;
int *pi = &ival; // pi points to an int
int **ppi = &pi; // ppi points to a pointer to an int
int *&r = p;	// r is a reference to the pointer p

Note!
To share a const object among multiple files, you must define the variable as extern.

Example:
extern const int bufSize = fcn();
constexpr:
- A constant expression is an expression whose value cannot change and that can be evaluated at compile time. A literal is a constant expression.
- Variables declared as constexpr are implicitly const and must be initialized by constant expressions.

Examples:
constexpr int mf = 20; // 20 is a constant expression
constexpr int limit = mf + 1; // mf + 1 is a constant expression
constexpr int sz = size(); // ok only if size is a constexpr	function

- Best Practices - generally, it is a good idea to use constexpr for variables that you intend to use as constant expressions.
- The types we can use in a constexpr are known as “literal types”.
- We cannot use a constexpr pointer to point to variables defined inside a function.
- It is important to understand that when we define a pointer in a constexpr declaration, the constexpr specifier applies to the pointer, not the type to which the pointer points.

Example:
const int *p = nullptr; // p is a pointer to a const int
constexpr int *q = nullptr; // q is a const pointer to int

type alias - is a name that is a synonym for another type. Type aliases let us simplify complicated type definitions, making those types easier to use.

Defining a type alias:
a) using typedef
typedef double wages; // wages is a synonym for double
typedef wages base, *p; // base is a synonym for double, p for	double*

Another example:
typedef int liczby_calkowite;
liczby_calkowite x = 10;
x += 10.6;
cout << x; // out: 20

b) using alias declaration (keyword ‘using’):
using liczby_calkowite = int; // liczby_calkowite is a synonym	for int

auto:
- auto tells the compiler to deduce the type from the initializer
auto item = v1 + v2; // item initialized to the result of v1 + v2

decltype - to define a variable with a type that the compiler deduces from an expression but do not want to use that expression to initialize the variable.

Example:
decltype(f()) sum = x; // sum has whatever type f returns

The way decltype handles top-level const and references differs subtly from the way auto does. When the expression to which we apply decltype is a variable, decltype returns the type of that variable, including top-level const and references.

Example:
const int ci = 0, &cj = ci;
decltype(ci) x = 0; // x has type const int
decltype(cj) y = x; // y has type const int& and is bound to x
decltype(cj) z; // error: z is a reference and must be	initialized

Warning!
Remember that decltype(( variable )) (note, double parentheses) is always a reference type, but decltype( variable ) is a reference type only if variable is a reference.

Example:
// decltype of a parenthesized variable is always a reference
decltype((i)) d; // error: d is int& and must be initialized
decltype(i) e; // ok: e is an (uninitialized) int

header guards – preprocessor directives to prevent multi including	of header files.

Example:
#ifndef SALES_DATA_H
#define SALES_DATA_H
#include <string>
struct Sales_data {
    std::string bookNo;
    unsigned units_sold = 0;
    double revenue = 0.0;
};
#endif

ways to initialize a string:

The string::size_type Type

Although we don’t know the precise type of string::size_type, we do know that it is an unsigned type (§ 2.1.1, p. 32) big enough to hold the size of any string. Any variable used to store the result from the string size operation should be of type string::size_type. Because size returns an unsigned type, it is essential to remember that expressions that mix signed and unsigned data can have surprising results.

auto len = line.size(); // len has type string::size_type

Advice: Use the C++ Versions of C Library Headers
In addition to facilities defined specifically for C++, the C++ library incorporates the C library. Headers in C have names of the form name .h. The C++ versions of these headers are named c name—they remove the .h suffix and precede the name with the letter c. The c indicates that the header is part of the C library.

Example:
#include <math.h>	# C style
#include <cmath>	# C++ style