C++ personal cheat sheet

0) general:

-> // - single line comments
-> /* … */ - multiple line comments
-> int main() {... return 0;} - starting point of program execution.
-> sizeof() - Yields the size in bytes of the object representation of type
sizeof(int)	# out: 4
-> using namespace …; - defining namespace
using namespace std;
-> using …; - enable to specify only what you need
using std::cin;
-> << - insertion operator
-> >> - extraction operator
-> const – declare constant variable, function
const int months_in_year {12};
-> static_cast<data_type>(variable) - explicit type casting
num3 = static_cast<double>(num1) / num2
-> !, &&, || - logical operators: not, and, or
within_bounds = (num > lower && num < upper) - important parenthesis for	logical expressions
-> && > || - && has precedence over ||, this means that parentheses are placed	to evaluate what would be evaluated together.

-> if, else if, else – conditionals
if (expr) {...;}
else if (expr) {...;}
else {...;}
-> (cond_expr) ? expr1 : expr2 - short form of ‘if’ statement
cout << num << " is " << ( (num %2 ==0) ? "even" : "odd" ) << endl;
-> switch – used for multiply if statements
switch(expression) {
  case constant-expression:
      statement(s);
      break;	//optional
   // you can have any number of case statements.
   default:	//Optional
      statement(s);	}
-> for (int i = 0; i < n; i++){...;} - basic for loop
for (int i {1}, j {5} ; i <= 5; ++i, ++j) {
cout << i << “ * “ << j << “ : “ << (i * j) << endl;
}
-> for (var_type var_name: sequence) {...;} - range-based for loops
for (auto/int score : scores)
cout << score << endl;
If the values stored in the range are expensive to copy, you may want to	use const auto &val.
for (const auto &val : values)
cout << val << endl;
-> while (expression) {...;} - basic while loop
-> do {...;} while (expression); - basic do-while loop
int number {};
do {
cout << “Enter an integer between 1 and 5: “;
cin >> number;
} while (number <= 1 || number >= 5);
-> abs() - return absolute value
int n = std::abs(-10);
-> (int)c / (char)n – conversion between int and char for letters eg. ‘a’
int n = (int)arr[i] + 1;
char c = (char)n;
-> (int)a – int(‘0’) – conversion from character digits to int (trick), if ‘a’	is a digit between 0-9
-> return_type function_name(parameters) {	- regular function
statements(s);
return 0;}
-> void function_name(parameters) {	- void function
statements(s);
return; // optional}
-> int multiply(int a, int b = 1); default values must be specified in function	declaration
-> int function_name(int a); - function prototype
-> void scale_number(int &num); - pass by reference
-> static – variable declared with keyword static preserves its value between	function calls
static int value {10};
-> inline - suggest to the compiler to compile function ‘inline’
inline int add_number(int a, int b) {...;}
-> nullptr; - a keyword denoting a null pointer constant. It can be converted to	any pointer or pointer-to-member type, yielding a null pointer of the	resulting type.

0) class:
-> this - is a pointer to the instance of the class on which the
function was called. this cannot be used in a static member function.

1) variables:

-> int age; - uninitiliazed (not a good practice)
-> int age = 21; - C-like initilization
-> int age (21); - Constructor initilization
-> int age {21}; - c++11 list initilization syntax; helps to catch an error,	recommended
-> unsigned/signed short int # at least 16 bits
-> unsigned/signed int # at least 16 bits
-> unsigned/signed long int # # at least 32 bits
-> unsigned/signed long long int # at least 64 bits
-> float – 7 decimal digits
-> double – 15 decimal digits
-> long double – 19 decimal digits
-> bool – true/false

2) pointers:

-> type *name {nullptr}; - pointer declaration
char *c {nullptr}; - points to nowhere
int *num; - uninitiliazed pointer points to ‘garbage data’
double *decimals {}; - initialized pointer, points to 0
int *num2_ptr {&num2};	// pointer to num2
-> *ptr; - pointer dereferencing
(*ptr).at(0) = 5;
ptr->at(1) = 10;
-> num2_ptr = nullptr; // 'nulling out' the pointer
-> dynamic memory allocation with ‘new’ and ‘delete’
int *int_ptr {nullptr};
int_ptr = new int;	// allocating an int on the heap
delete int_ptr;	// frees the allocated storage
-> dynamic memory allocation for an array
int *array_ptr {nullptr};
array_ptr = new int[size];	// allocate array on the heap
delete [] array_ptr;	// frees allocated storage
-> const int *score_ptr {&high_score}; - pointers to constant
-> int *const score_ptr {&high_score}; - constant pointer
-> passing pointers to a function (pass-by reference)
void double_data(int *int_ptr) {*int_ptr *= 2;}
-> return a pointer from a function
int *create_array(size_t size, int init_value = 0);

a) climits:

-> #include <climits>
-> INT_MIN / INT_MAX – minimum, maximum value of variable. Other popular	possibilities: CHAR, SHRT, LONG)

a) cmath:

-> #include <cmath>
-> pow(val, pow) – raises to a given power
-> round(val) – rounds to the nearest int value
mean_val = round(mean_val * 100) / 100;
-> log2
-> sqrt
-> ceil
-> floor
-> sin
-> cos
-> tan
-> abs() - return absolute value from expression
std::abs(a-b);
-> fmin(a, b) – return min of two values
std::fmin(5, 10)	# out: 5
-> fmax(a, b) – return max of two values
std::fmax(5, 10)	# out: 10

b) iostream:

-> #include <iostream>
-> cout – print output to the console
-> cin – take input from the keyboard
-> endl – insert “\n”

c) iomanip:
-> std::boolalpha # will display true/false
-> std::noboolalpha # will display 1/0
-> std::showpos # show plus with positive numbers
-> std::resetiosflags() # reset to default
std::cout.resetiosflags(std::ios::boolalpha);
-> std::cout.setf() # set format flags
std::cout.setf(std::ios::showpos);
-> std::cout.unsetf() # unset format flags
std::cout.unsetf(std::ios::scientific | std::ios::fixed);
-> std::dec, std::hex, std::oct – displaying using different basis
std::cout << std::hex << num << std::endl;
-> std::cout.setf() # set format flags
std::cout.setf(std::ios::showpos);
-> std::setprecision() # number of digits displayed, default 6 for floats
-> std::fixed # fixed to a specific number of digits after the decimal point
td::cout << std::setprecision(3) << std::fixed;

c) cctype:

-> #include <cctype>
-> isalnum - checks if character is alphanumeric
-> isalpha - checks whether c is an alphabetic letter
std::isalpha(str[i]))
-> isdigit – checking if char is a digit, return bool
-> islower – checking if char is lowercase, return bool
-> ispunct - check if character is a punctuation character
-> isspace - checking if char is a white-space, return bool
-> isupper - checks if character is uppercase letter
-> tolower – converts given char to lowercase
std::tolower(‘A’)	# out: ‘a’
-> toupper - converts given char to uppercase

d) string:

-> #include <string>
-> std::string s1 {s2};	- creating string s1 as a copy of s2
-> std::string s1 {s2, 3}; - s1 = s2[0:3]
-> std::string s1 {s2, 1, 2}; - s1 = s2[1:3]
-> std::string s1 = s2.substr(3, 2); - creating string as substring of s2
-> at() - accesses the specified character with bounds checking
-> front() - accesses the first character
-> back() - accesses the last character
-> empty() - check whether string is empty, return true or false
-> length/size() - return size of string
-> clear() – removes content of string object
-> assign() - assign characters to a string
s.assign(4, '=');	# out: “====”
std::string const c("Exemplary");
s.assign(c, 0, c.length()-1);	# out: "Exemplar"
-> insert - inserts characters
s.insert(6, "a");
-> erase(size_t pos = 0, size_t len = npos) - Erases part of the string,	reducing its length.
str.erase (10,8);
str.erase (str.begin()+5, str.end()-9);
-> push_back – append character to the end of string
-> pop_back() - removes the last character, return none value
-> append(str) - appends characters to the end
str.append("-inator ");
-> compare
-> replace(size_type pos, size_type count, const basic_string& str) - replaces	specified portion of a string
str.replace(10, 5, "red");
-> substr(size_t pos = 0, size_t len = npos) - Returns a newly constructed	string object with its value initialized to a copy of a substring of this	object. The substring is the portion of the object that starts at	character position pos and spans len characters (or until the end of the	string, whichever comes first).
std::string str="We think in generalities, but we live in details.";
std::string str2 = str.substr (3,5);	# out: "think"
-> find(substr) - Searches the string for the first occurrence of the sequence	specified by its arguments, return size_t or std::string::npos
std::size_t found = str.find(str2);
-> find_last_of() - finds the last character equal to one of characters in the	given character sequence.
link.find_last_of("/");
-> rfind - find last occurrence of content in string.
-> std::string::npos - maximum value for size_t.
-> stoi – converts string to integer
std::stoi(“123”);	# out: 123
-> stol
-> stof – converts string to float
-> stod
-> to_string - converts an integral or floating point value to string
std::to_string(15);
-> getline(std::cin, name, [delimiter]) - Get line from stream into string
std::getline(cin, s1)

e) iterator:

-> #include <iterator>
-> begin/rbegin – iterator pointing at the first element or first reversed
-> end/rend - iterator pointing at the last element or last reversed
-> advance(InputIt& it, Distance n) - increments given iterator it by n	elements.
std::advance(first, 2); // advance the iterator 2 position
-> next - return the nth successor of iterator it.
auto nx = std::next(it, 2);
-> prev - decrement an iterator
auto pv = std::prev(it, 2);

-> back_inserter – returns an iterator which can be used to add elements to the	end of the container
std::copy(arr.begin(), arr.end(), std::back_inserter(sortedArr));
-> front_inserter - Constructs a front-insert iterator that inserts new elements	at the beginning of x. The type of x needs to have a push_front member	function (such as the standard containers deque and list).
std::copy(nums.begin(), nums.end(), std::front_inserter(deq));

f) algorithm

-> any_of(InputIt first, InputIt last, UnaryPredicate p) - checks if a predicate	is true for any of the elements in a range
if(std::any_of(temp.begin(), temp.end(), [](int i){return i == 1;}))
-> copy(InputIt first, InputIt last, OutputIt d_first) - Copies the elements in	the range, defined by [first, last), to another range beginning at	d_first.
std::copy(from_vector.begin(), from_vector.end(),	std::back_inserter(to_vector));
-> count(InputIt first, InputIt last, const T &value) - Returns the number of	elements in the range [first, last) satisfying	specific criteria.
total += std::count(t.begin(), t.end(), 1)
-> includes(InputIt1 first1, InputIt1 last1, InputIt2 first2, InputIt2 last2) -	Returns true if the sorted range [first2, last2) is a subsequence of the	sorted range [first1, last1).
std::includes(arr2.begin(), arr2.end(), arr1.begin(), arr1.end());
-> find(InputIt first, InputIt last, const T &value) – returns iterator to the	first element satisfying the condition or last if no such element is	found.
auto result1 = std::find(std::begin(v), std::end(v), n1);
-> for_each(InputIt first, InputIt last, UnaryFunction f) - applies a function	to a range of elements.
std::for_each(str1.begin(), str1.end(),[](char& c){c= std::tolower(c);});
-> max_element(InputIt first, InputIt last) – returns an iterator to max element	in a container
auto it = std::max_element(arr.begin(), arr.end());
-> remove(ForwardIt first, ForwardIt last, const T& value) - Removes all	elements satisfying specific criteria from the range [first, last) and	returns a past-the-end iterator for the new end of the range.
Example of erase-remove idiom !!!
str1.erase(std::remove(str1.begin(), str1.end(), ' '), str1.end());
-> reverse(InputIt first, InputIt last) – returns a reversed container
std::reverse(arr.begin(), arr.end());
-> rotate(ForwardIt first, ForwardIt n_first, ForwardIt last) – performs a left	rotation on a range of elements
std::rotate(arr.begin(), arr.begin() + 3, arr.end());
-> set_intersection(InputIt1 first1, InputIt1 last1, InputIt2 first2, InputIt2	last2, OutputIt d_first) - computes the intersection of two sorted	containers
std::set_intersection(v1.begin(), v1.end(),
        v2.begin(), v2.end(),
        std::back_inserter(v_intersection));
-> sort((RandomIt first, RandomIt last, Compare comp) - Sorts the elements in	the range [first, last) in non-descending order. The order of equal	elements is not guaranteed to be preserved. A sequence is sorted with	respect to a comparator comp.
std::sort(s.begin(), s.end(), [](int a, int b) {return a > b;});

-> transform(InputIt first1, InputIt last1, OutputIt d_first,UnaryOperation	unary_op) - applies the given function to a range and stores the result in	another range, beginning at d_first. Std::transform does not guarantee in-	order application of unary_op or binary_op.
std::transform(arr.begin(), arr.end(), std::back_inserter(v_str),
[](int num) -> std::string {return std::to_string(num);});
-> unique(ForwardIt first, ForwardIt last) - removes consecutive duplicate	elements in a range
Example of erase-remove idiom !!!
v.erase(std::unique(v.begin(), v.end()), v.end());

g) vector

-> #include <vector>
-> std::vector<int> v {10, 0}; - list initialization, out: 2 elements {10, 0}
-> std::vector<int> v (10, 0); - constructor initialization, out: 10 elements	initialized to 0
-> v.at(element_index) - method to access a vector element
-> v.front() - reference to the first element in the vector
-> v.back() - reference to the last element in the vector
-> v.size() - return length of the vector as size_type
-> v.empty() - checks if the container has no elements
-> v.push_back(element) - add a new element to the end of the list
-> v.pop_back() - removes the last element in the vector, effectively	reducing	the container size by one
-> v.clear() - erase all elements from the container.

h) map

-> #include <map>
-> std::map<char, int> m {}; - initialization
-> find() - return it to the element, if not found returns m.end() iterator
auto it = m.find(‘l’);
it.first = ‘l’;
it.second = 1;

i) set

-> #include <set>
-> std::set<char> s; - set initialization
-> size() - returns number of elements;
-> insert() - insert element to set
-> count() - returns the number of elements matching specific key

j) numeric

-> #include <numeric>
-> accumulate(( InputIt first, InputIt last, T init, BinaryOperation op) -	Computes the sum of the given value init and the elements in the range	[first, last).
int product = std::accumulate(v.begin(), v.end(), 1,	std::multiplies<int>());

k) cassert

-> #include <cassert>
-> assert((switchNotation(assert_inp_2, "tally") == assert_res_2)); // important	double parenthesis

Page 34 classess